Barycentric Coordinates
Any point on a triangle can be expressed as q={ ap1+bp2+cp3 | a+b+c=1, a,b,c >=0}
If != 1, outside the plane. If <0, inside plane but outside triangle
Used for ray-tracing intersections
Used for interpolating triangle information, often based on vertices rather than triangle
Come back to this...may want to just write out by hand

Rendering Pipeline
Inverse of ray-casting: send rays from the scene into the camera
Pick polygon and determine what pixels it affects
Pipeline stages:
Modeling Transform – transform into 3D world coords
Camera Transform – transform into 3D camera coords
Lighting – Illuminate according to lighting and reflectance
Projection transform – transform to 2D camera coord
Clipping – clip primitives outside camera view
Scan Conversion – draw pixels (textures, hidden surface, ect.)
Viewing transform alg
Projection – map 3D camera coords to 2D screen coords
Parallel – direction of projection (DOP) same for all points. Rays oriented parallel to each other. Relative proportions preserved, angles not preserved. Less realistic, far objects don't get smaller. Orthographic and oblique.
Parallel Projection matrix
Perspective – map points onto view plane along projectors emanating from a center of projection (COP). Not a real projection, not a linear map from 3D to 2D. Parallel lines do not remain parallel.

Clipping and Scan Conversion
Draw primitives only inside window of scene
Point is easy – determine if inside boundaries.
Cohen-Sutherland line clipping
Polygons: Sutherland-Hodgeman Clipping - Clip each window boundary one at a time. Do inside test for each point in sequence, insert new point when crossing window boundary, remove outside points.
Scan conversion – set pixel colors to match the primitive. Must be fast and not allow cracks between adjacent prims.
Inside Triangle Test – point is in a triangle if its in the positive half-space of all three boundaries.
Triangle Sweep-Line – Compute which pixels are inside using horizontal spans. Process spans in scan-line order. Use edge slopes to update coordinates incrementally. Takes advantage of spatial coherence and edge linearity. Does not work for some polygons.
Odd-parity Rule – if inside, any ray from P to infinity crosses an odd number of edges. Problem with self intersecting polygons.
Polygon Sweep-Line – incremental algorithm to find spans, determine “insideness” with odd parity rule
Edge pixels can cause aliasing whether on or off. Can display at higher res OR adjust pixel intensity on edges.
Prefiltering – calculate percent pixel coverage and multiply by desired color. Supersampling – sample as if higher res, average samples, aka bilinear interp.

Shading and Visibility
Flat – lighting equation constant over surface. Spatial coherence. AL light direction, flay polygon, viewed from infinitely far away.
Gouraud – normal at each vertex with one calculation per vertex, bilinearly interpolate surface from vertex colors down and across scanlines. Trouble with large polygons/high frequency light changes.
Phong – One lighting calc per pixel, bilinearly interpolate normals down and across scan lines.
Hidden Surface Removal – don't want to draw surfaces no visible to viewer.
Back face – dot product of normal and view directions. V dot N > 0, back face. After model transform
Painter's – sort front to back, draw back first, over write with front pixels as processed. Can't always sort prims
BSP Tree – Draw objects on furthest side of a plane first
Ray cast – cast ray for each pixel, take closest intersection. After modeling transform
Z Buffer – store color and depth, update only when depth is closer than in buffer. Depth interpolated from verts. Use in scan conversion
A-Buffer – linked list of surfaces at each pixel for better transparency support, helps with AA
Scan conversion interp example

Textures
Texture elements called texels, 4 bytes (rgba) each. Each vertex mapped to part of image. Added to poly in scan conversion.
Parameterization: how do we decide where on geometry to match each color?
Unfold/map entire surface
Atlas – break model into 'pieces' to texture
Mapping – interpolate tex coords down/across scanlines with a perspective divide
Filtering – transform from screen to texture space does not preserve area, computer average of texture pixels to get screen color. Size of filter depends on projective deformation.
Mip Maps – prefiltered for multiple resolutions. Faster, more memory. Trade aliasing for blurring. Isotropic, doesn't take differences in vert and horizontal compression.
Summed Area – approximate summation/integration over arbitraty region by summation/integration over an axis aligned one. Perform quickly by precomputing integrals. Formula. Each texel is sum of all texels below and to the left.
Modulation textures – map tex values to lighting scale factor
Illumination mapping – map to any material param.
Bump mapping – store changes to normals in a tex map.
Enviroment mapping – generate spherical/cubic map of environment around the model
Solid textures – tex value indexed by 3D location

3D Object representation
Point Cloud – unstructured set of 3D points
Range Image – image storing depth instead of color
Polygon Soup – unstructured set of polygons
Mesh – connected set of polygons
Subdivision surface – coarse mesh + subdivision rule
Parametric surface – Tensor product spline patches
Implicit surface – points satisfying F(x,y,z) = 0;
Voxels – uniform grid of volumetric samples
BSP Tree – BSP with solid cells labeled, constructed from polygon representations
Constructive Solid Geometry (CSG) – hierarchy of boolean ops applied to simple shapes
Sweep – solid swept by curve along trajectory
Scene Graph – union of objects at leaf nodes
Skeleton – graph of curves with radii

Subdivision Surfaces
Refinement (add new verts and connect) and Smoothing (move vert positions).
Loop subdivision – subdivide each tri into 4 tris, new location as weighted average of original vertex and its neighbors
Subdivision formula?
Subdivision matrix – computer new positions as linear combination of previous ones
Store the mesh, aim for efficiency and subdivision implementation
Independent faces – each face lists vertex coords. Redundant verts, no topology
Vertex Face Tables – each face lists vertex references. Still no topology
Adjacency Lists – store all vertex, edge, face adjacencies. Efficient traversal, extra memory, variable array size
Winged Edge – adjacency encoded in edges.

Parametric Curves
Splines – mathematical way to express curves
Loftsmans's spline was a long, narrow strip of wood/plastic used to fit curves through specific data points. Shaped by lead weights called ducks, gives smooth curves.
CG Spline – a piecewise polynomial function whose derivatives satisfy some continuity constraints across curve boundaries.
Piecewise – spline is a collection of individual segments
Polynomial functions – each segment expressed by polynomial function.